## Slide 1: Machine Check Exception
NISHANSHI SHUKLA
(121030)

## Slide 2: Machine Check Exception
Machine check exception indicates that the working processor has detected an error in the hardware or in the bus.
Most common reasons for machine check exceptions are system bus errors, memory cache errors, inadequate memory errors or inappropriate heating or cooling of the system.
Machine check exception is generated when error information is loaded onto machine check registers.
There are two types of machine check exceptions, correctable and uncorrectable.
Machine check exceptions are difficult to debug mostly because of the large number of potential causes like violation to board design guidelines, operating the processor out of specification, incorrect hardware installation or BIOS setup issue.

## Slide 3: Machine Check Architecture
Some processors implement machine check architecture for detecting and reporting hardware i.e. machine errors.
A set of model specific registers are used to do machine checking and recording the detected errors.
The detection of an uncorrected machine check error is signaled by the processor by generating a machine check exception, which is an abort class exception.
Machine check exception handler can collect information about the machine check error from the machine check model specific registers.
Machine check architecture communicates critical hardware errors to software and to possibly recovery from catastrophic system failures.

## Slide 4: MCE log tool
Mcelog is the user space backened for logging machine check errors reported by the hardware to the kernel.
Mcelog decodes the errors and manages various other responses like off lining memory or triggering events.
It also handles the corrected errors by logging and accounting them. But primarily it handles the machine checks and thermal events which are reported for errors by the processor.
Mcelog runs on several modes like cronjob, trigger and daemon.
In cronjob, it runs every five minutes from cron and checks for errors.
In trigger, kernel runs the it when some error occurs.
In daemon mode it runs continuously as a daemon in the background and waits for errors.

## Slide 5: References
Intel® 64 and IA-32 Architectures Software Developer’s Manual Volume 3A: System Programming Guide, Part 1, order number: 253668-039US, May 2011.
Intel® Embedded Debugging Machine Check Exceptions on Embedded IA Platforms, White Paper: Ashley Montgomery (Platform Application Engineer Intel Corporation), Tian Tian (Platform Application Engineer Intel Corporation), July 2010.
http://www.advancedclustering.com/act-kb/what-are-machine-check-exceptions-or-mce/
mcelog: memory error handling in user space, Andi Kleen, Intel®Corporation.
http://www.mcelog.org/README.html

## Slide 6: Thank You!